## Slide 1
Developed in partnership with
Notes: (Holding Slide)

## Slide 2
THE REACTION TRACKER
1
2
3
Get hands-on with the Reaction Tracker!
How fast are you?
1
THE MULTI-MOVER
Code the Multi-Mover to move and deliver to key locations on the airbase
SMART SENSORS
Code the Multi-Mover sensors to collect, deliver and pass cargo on the airbase
3
4
GEAR UP, GEAR DOWN
Gears and forces –
build and code for
speed or power!
Notes: Celebrate the success pupils have had in Coding Success 5 so far!
Introduce Mission 4

## Slide 3
MISSION 4: AIM
Explore what gear ratio is
Test how different gear combinations perform in different real-world challenges
Understand how different gearing affects speed and force (torque)
Explore how combining gears in different combinations can affect speed and strength
Notes: Briefly introduce the Aim of Mission 4.

## Slide 4
Today we’re going to be engineers! We’re going to look at how machines use gears to either go really, really speedy… or to be super strong.
A gear is like a wheel with teeth. When two gears touch, one makes the other turn. But here’s the clever bit - if the gears are different sizes, they can change how fast (speedy) something turns, or how strong something turns. Let’s take a closer look…
SPEEDY OR STRONG?
EXPLORING GEARS…
Notes: Introduce the context of Mission 4.

## Slide 5
A CLOSER LOOK: GEARING DOWN
The motor turns the small gear which has 12 teeth.
The teeth transfer the force from one gear to another.
This gear has 36 teeth so turns 3 times slower than the first gear but with 3 times more torque (turning force).
What do you notice about the direction of each gear?
Click to see the gears move
Driver Gear
Driven Gear
STRONG
Notes: Emphasise that the small gear is the driver because it’s connected to the motor.
Explain that the small gear spins fast and turns the big gear (the driven gear) more slowly.
Highlight the trade-off: the big gear turns 3× slower but has 3× more torque (turning force).
Relate this to real-life examples, e.g. bicycle gears when climbing a hill – slower but more powerful.
Point out that gears reverse direction: if the driver turns clockwise, the driven turns anti-clockwise.
Reinforce vocabulary: driver, driven, torque, gearing down.

## Slide 6
A CLOSER LOOK: GEARING UP
The motor turns the large gear which has 36 teeth.
The teeth transfer the force from one gear to another.
This gear has 12 teeth so turns 3 times faster than the first gear but with 3 times less torque (turning force).
What do you notice about the direction of each gear?
Click to see the gears move
Driver Gear
Driven Gear
SPEEDY
Notes: Explain that the big gear is the driver because it’s connected to the motor.
Show that the big gear turns a small gear (the driven gear) which spins faster – in this case, 3× faster.
Highlight the trade-off: the small gear spins quickly but has less torque (less turning force).
Relate this to real-life examples, e.g. bicycle gears when riding downhill or on flat ground – faster but less powerful.
Point out that gears reverse direction: if the driver turns clockwise, the driven turns anti-clockwise.
Reinforce vocabulary: driver, driven, torque, gearing up.

## Slide 7
Bike on a flat surface "whirrrr-click-click" (fast pedalling noise)
Sports car in top gear "VROOOOOM!"
Tin Opener “Krrrk-chhh! Krrrk-chhh!”
Bulldozer "BRRRRrrrRUMMM”…"scrrrunch")
Bike up hill "chunk-chunk" (slow pedalling uphill)
Tank "clank-clank-clank" and a low "grrrr"
SPEEDY
STRONG
Notes: Explain that the slide shows different machines or situations where gears are used.
The left side represents SPEEDY (high speed, low torque) and the right side represents STRONG (low speed, high torque).
Tell pupils: "Each example will appear in the middle first. Your job is to guess – does this need SPEED or STRENGTH?"
Encourage them to think about what the job needs:
  Going fast but not needing much force → SPEEDY
  Going slowly but needing lots of power → STRONG
Once they guess, click to animate so the answer moves to the correct side.
Use the sounds (e.g., “VROOOOM!” or “clank-clank-clank”) to make it fun and memorable.
Reinforce the link to gearing up (SPEEDY) and gearing down (STRONG).

## Slide 8
Notes: Play animation (21 sec) to show pupils how SPIKE SPEEDY and SPIKE STRONG were constructed using LEGO Education SPIKE Prime.
Reveal the pre-built SPIKE SPEEDY and SPIKE STRONG vehicles.

## Slide 9
GEARED DOWN: SPIKE STRONG
SPIKE SPEEDY Vs SPIKE STRONG Same Motors. Different Gearing.
GEARED UP: SPIKE SPEEDY
Notes: Show the gear setups on the two models and let pupils examine them.

## Slide 10
SPIKE STRONG’S GEARS: Gearing Down!
The motor turns the small gear which has 12 teeth.
The teeth transfer the force from one gear to another.
This gear has 36 teeth so turns 3 times slower than the first gear but with 3 times more torque (turning force).
What do you notice about the direction of each gear?
Click to see the gears move
Driver Gear
Driven Gear
STRONG
Notes: We looked at this setup earlier on. This is the setup for SPIKE STRONG.
Ask pupils: What do you notice about the direction of each gear?
Answer: When two gears touch each other, they always spin in opposite directions.

## Slide 11
SPIKE SPEEDY’S GEARS: GEARING UP!
SPIKE SPEEDY uses two pairs of gears to go really fast...
The grey gear has 28 teeth which then turns the beige gear which has 20 teeth.
This gear has 12 teeth so turns 3 times faster than the first gear and is connected with an axle to the grey gear.
Click to see the gears move
This is the driving gear which is connected to the motor. It has 36 teeth.
The beige gear turns 1.4 times faster than the grey gear.
Driver Gear
Driven/Driver Gear
Driven/Driver Gear
Driven
What do you notice about the direction of each gear?
Notes: This is the setup for SPIKE SPEEDY. The principle is the same as the gearing up example we looked at earlier BUT it is now MORE geared up. Gear Pair 1:
Driver: Gear A (36 teeth, connected to motor)
Driven/Driver: Gear B (12 teeth, driven by Gear A, drives Gear C via axle)
Gear Pair 2:
Driven/Driver: Gear C (28 teeth, driven by Gear B via axle, drives Gear D via teeth)
Driven: Gear D (20 teeth, final output)
Ask pupils: What do you notice about the direction of each gear?
When two gears touch each other, they always spin in opposite directions.
You can demonstrate this with the animation
In this gear train, the black 36T turns one way (clockwise), the black 12T turns the other way (anticlockwise), the grey 28T is connected to the black 12T so turns the same way (anticlockwise), and the beige 20T turns opposite to the grey 28T (clockwise) so is now going in the same way as the first gear
Tip for teaching:
Relate it to a “double boost” in a racing game - first boost from the first gear pair, second boost from the second pair.

## Slide 12
Gear ratio tells us how fast or strong something will turn when one gear moves another.
Gear Ratio = Teeth on the driven gear ÷ Teeth on the driver gear
WHAT’S THE GEAR RATIO ON SPIKE STRONG?
Gearing Down (for Strength/Torque)
Driver Gear: 12 teeth
Driven Gear: 36 teeth
Gear Ratio = 36 ÷ 12 = 3
This means:
The driven gear turns slower, but with 3 times more force.
Notes: This is the gear ratio for SPIKE STRONG. Gear ratios are calculated using the number of teeth on each gear
The driver gear has 12 teeth
The driven gear has 36 teeth
The gear ratio is calculated using a calculation: gear ratio = teeth on driven gear divided by teeth on the driver gear
Gear ratio: A gear ratio of 3 means the driven gear produces 3 times more force but rotates 3 times slower than the driver gear

## Slide 13
Gear ratio tells us how fast or strong something will turn when one gear moves another.
Gear Ratio = Teeth on the driven gear ÷ Teeth on the driver gear
WHAT’S THE GEAR RATIO ON SPIKE SPEEDY?
FIRST PAIR OF GEARS
Driver Gear: : 36 teeth
Driven Gear: 12 teeth
Gear Ratio = 12 ÷ 36 = 0.33
SECOND PAIR OF GEARS
Driver Gear: 28 teeth
Driven Gear: 20 teeth
Gear Ratio = 20 ÷ 28 = 0.71
OVERALL GEAR RATIO Multiply them together
Gear Ratio = 0.33 x 0.71= 0.24
Notes: This is the gear ratio for SPIKE SPEEDY. Gear ratios are calculated using the number of teeth on each gear. SPIKE SPEEDY uses two pairs of gears so we have to calculate two gear ratios and then multiply them together at the end
The first driver gear has 36 teeth
The first driven gear has 12 teeth
The gear ratio is calculated using a calculation: gear ratio = teeth on driven gear divided by teeth on the driver gear
First pair gear ratio: A gear ratio of 0.33 means the driven gear produces 0.33 times the original force but rotates 3 times faster than the driver gear
The second driver gear has 28 teeth
The second driven gear has 20 teeth
The gear ratio is calculated using a calculation: gear ratio = teeth on driven gear divided by teeth on the driver gear
Second pair gear ratio: A gear ratio of 0.71 means the driven gear produces 0.71 times the original force but rotates 1.4 times faster than the driver gear
The overall gear ratio is calculated by multiplying the two gear ratios together: 0.33 x 0.71 = 0.24. This means the driver gear is 0.24 times slower than the final driven gear (or the final gear moves 4.2 times quicker than the motor)

## Slide 14
SPEEDY
STRONG
CODING…
Because the gears in SPIKE STRONG are arranged differently, they make the wheels turn the opposite way to SPIKE SPEEDY’s. That’s why we need to use a negative velocity for SPIKE STRONG - it tells the motor to spin the other way so it still goes forward.
Notes: SPIKE STRONG has only two gears — one on the motor and one on the wheel axle. Because there’s just one gear mesh, the wheels turn in the opposite direction to the motor.
SPIKE SPEEDY has four gears arranged in two pairs. Each mesh reverses direction, so with two reversals, the wheels end up turning the same way as the motor.
This is why SPIKE STRONG needs a negative speed in the program to move forward, while SPIKE SPEEDY can use a positive speed.

## Slide 15
Notes: Explain that the class is going to explore the impact of gears by playing two ‘games’ with SPIKE SPEEDY and SPIKE STRONG

## Slide 16: SPIKE SLEDGE: THE EXPERIMENT
“We’re going to race SPIKE SPEEDY and SPIKE STRONG, each pulling a sledge. The sledges will be loaded with different volumes of water to change how heavy they are to pull.
Before each race, you’ll guess which robot will win — will it be the fast but weaker SPIKE SPEEDY, or the slower but stronger SPIKE STRONG?”
Notes: Introduce the SPIKE Sledge Experiment.

## Slide 17
SPEEDY
STRONG
EXPERIMENT ONE: LIGHT LOAD
100ml of water
“Alright, team - we’ve only got 100ml of water in the sledge, so it’s nice and light! Which robot do you think will win: the lightning-fast SPIKE SPEEDY or the powerhouse SPIKE STRONG? Get READY, LEGO, GO!”
Notes: SET UP RACETRACK – two lines 2 metres apart.
AFTER EXPERIMENT ONE…
Highlight that with a light load, speed is the advantage - less torque is needed, so SPIKE SPEEDY’S gearing-up design works well.
Emphasise how gear choice changes performance, and that different setups are better for different tasks.
Reinforce the key idea: gearing up increases speed but reduces turning force.

## Slide 18
SPEEDY
STRONG
EXPERIMENT TWO: MEDIUM LOAD
500ml of water
“Alright, team - this time the sledge is carrying 500ml of water, so it’s a bit heavier. Which robot will handle it better - the lightning-fast SPIKE SPEEDY or the strong, steady SPIKE STRONG? Get READY, LEGO, GO!”
Notes: AFTER EXPERIMENT TWO…
Point out that with a medium load, the race is more balanced — speed and torque both matter.
Encourage pupils to notice if SPIKE SPEEDY slowed down more or if SPIKE STRONG caught up compared to the lighter load race.
Reinforce that gear setup affects how well a robot copes with extra weight, not just how fast it can go.

## Slide 19
SPEEDY
STRONG
EXPERIMENT THREE: HEAVY LOAD
1000ml of water
“Alright, team - now we’ve loaded the sledge with 1000ml of water. This is the heaviest challenge yet - will SPIKE SPEEDY manage it, or will SPIKE STRONG power ahead? Get READY, LEGO, GO!”
Notes: AFTER EXPERIMENT THREE…
Highlight that with a heavy load, torque becomes the key advantage, and SPIKE STRIONG’S gearing-down design provides the extra turning force needed to get moving.
Point out that SPIKE Speedy may not have had enough strength/torque to overcome the starting resistance — a real-world example of why strong gearing is used in machinery for heavy work.
(OPTIONAL) Next Steps for Teaching:
Investigate the tipping point: Gradually increase the weight in smaller steps to find the exact load where SPIKE SPEEDY stops moving — great for talking about limits and measurement.
Time the races: Use stopwatches to record how long each robot takes for the same load, then make a bar chart to compare performance.
Change the gear setup: Let pupils swap gears on the robots and predict how it will affect speed and strength.
Explore friction: Try the same loads on different surfaces (carpet, wood, smooth plastic) and discuss how surface resistance affects performance.
Real-world links: Compare to bicycles, cars, or construction vehicles, and discuss why engineers choose different gear ratios for different jobs.
Maths connection: Have pupils calculate ratios and speeds, reinforcing multiplication and division skills.

## Slide 20
EXPERIMENT FOUR: RAMP 10 DEGREES
STRONG
SPEEDY
“We’re now removing the sledge and putting the robots on a ramp set at 10 degrees and asking: Who will reach the top first - the fast but less powerful SPIKE SPEEDY or the slower but stronger SPIKE STRONG? Get READY, LEGO, GO!”
Notes: SET UP A RAMP (card, wood, table) – using the angle specified
AFTER EXPERIMENT FOUR…
Point out that the ramp causes more of the robot’s weight to add resistance, so the robots now need both forward movement and extra strength/torque to push uphill
Encourage pupils to notice if Speedy slowed down more on the incline or if Strong’s extra torque helped it climb steadily
Link to real-life examples like cycling uphill or cars climbing hills, where lower gears give more strength to overcome slopes

## Slide 21
STRONG
SPEEDY
EXPERIMENT FIVE: RAMP 20 DEGREES
“Alright, team - we’re cranking up the challenge! The ramp is now set to a steep 20 degrees - will SPIKE SPEEDY have the speed to get there, or will SPIKE STRONG’S torque win the climb? Get READY, LEGO, GO!”
Notes: AFTER EXPERIMENT FIVE…
Highlight that the steeper ramp increases the effect of gravity, so more torque is needed to keep moving
Draw attention to any change in behaviour — for example, SPIKE SPEEDY slowing right down or stopping, while SPIKE STRONG keeps climbing steadily
Link to real-world situations where steep hills require lower gears in bikes or vehicles to provide enough turning force

## Slide 22
EXPERIMENT SIX: RAMP 30 DEGREES
STRONG
SPEEDY
“Alright, team - this is it, the ultimate challenge! The ramp is now a huge 30 degrees - will SPIKE SPEEDY even make it off the start, or will SPIKE STRONG power its way to the top? Get READY, LEGO, GO!
Notes: AFTER EXPERIMENT SIX…
Emphasise that at very steep angles, the effect of gravity is much stronger than the robot’s forward push, so high torque is essential.
Point out that SPIKE SPEEDY’S gearing-up sacrifices torque, which is why it may barely move or stall completely.
Show how SPIKE STRONG’S gearing-down gives it the torque needed to keep turning the wheels, even on steep slopes.
Connect to real-life examples such as trucks using low gear on steep roads or cyclists standing up and shifting to low gear to power up hills.
(OPTIONAL) Next Steps for Teaching:
1. Vary the load on the ramp
Try the same ramp angles with different weights added to the robot to see how speed and torque interact with gravity and load.
Pupils can predict which robot will succeed or fail at each combination.
2. Measure performance
Time how long each robot takes to reach the top at different ramp angles.
Plot a graph of ramp angle vs time or vs “success/failure” to make patterns visible.
3. Change the gearing
Let pupils swap gears on SPIKE Speedy or SPIKE Strong and re-test to see how gear ratios change climbing ability.
4. Explore friction
Test on ramps with different surfaces (smooth plastic, carpet, sandpaper) to see how grip affects the result.
5. Real-world link
Compare the robots’ behaviour to cars, trucks, and bikes on hills — why do vehicles use lower gears for steep climbs?

## Slide 23
SPIKE SPEEDY
SPIKE STRONG
1
2
WHAT HAPPENED?
SPIKE SPEEDY is designed to move quickly over a distance (like a race car) so it is geared up for speed. It won the race on a flat track without a heavy load – but it struggled moving up the steep ramp.
Whereas SPIKE STRONG is designed to carry a heavy load and move slowly, uphill (a bit like a tractor). SPIKE STRONG is geared down (for torque/strength). Moving up the ramp was no problem!
Speed and strength are a trade-off: you can’t have maximum of both at the same time!
Notes: Give an overview of the key outcomes of the experiments

## Slide 24
MISSION 4: REVIEW
I understand what gear ratio is
I have used testing to discover how different gear combinations perform in real-world challenges
I understand how different gearing affects speed and force (torque)
Explore how combining gears in different combinations can affect speed and strength
Notes: Briefly review the Aim of Mission 4.

## Slide 25
By taking part in the four Coding Success 5 Missions, we have learned that being fast isn’t just about zooming around - it’s about working together, thinking carefully, and using our skills to find our Smart Speed.
We saw that coding the right attachments and sensors or using the right gear combinations, can make a robot super reliable, super quick or super strong… and the best robot will depend on what job it’s doing.
When we use our human skills like communication, problem-solving, resilience and teamwork - along with the right attachments, code and robot design - we can be successful and achieve our Smart Speed!
Notes: Reminder of key outcomes of the 4 Missions:
Mission 1 – Human Attributes: Tested reaction times to light and sound, building awareness of human reactions, processing speed and decision-making under pressure.
Mission 2 – Movement & Mechanical Advantage Programmed robots to navigate a mat at a smart speed, introducing the concept of mechanical advantage through different attachments.
Mission 3 – Technical Advantage: Incorporated sensors to help robots make quick, accurate decisions — proving that “thinking” can be just as important as moving fast.
Mission 4 – Gears for Speed or Strength: Explored how gear combinations can change robot performance, choosing speed for quick tasks and torque for heavy lifting.

## Slide 26
CONGRATULATIONS!
Notes: Present pupils with certificates and congratulate them on their coding success!

## Slide 27
THE REACTION TRACKER
1
2
3
Get hands-on with the Reaction Tracker!
How fast are you?
1
THE MULTI-MOVER
Code the Multi-Mover to move and deliver to key locations on the airbase
SMART SENSORS
Code the Multi-Mover sensors to collect, deliver and pass cargo on the airbase
3
4
GEAR UP, GEAR DOWN
Gears and forces –
build and code for
speed or power!
Notes: Coding Success 5: complete!

## Slide 28
CODING SUCCESS: CLUB
THE CHALLENGE
Design, build, and code a SPIKE Prime robot for two gym events:
Speed Sprint – 2 Metre Dash
Race 2m in the shortest possible time.
Flat track, smooth surface
Sensors stop the robot at the finish
Power Lift – Ramp Climb
Pull a weighted trailer up an incline
Must reach the top without stalling or rolling back
What is the steepest incline you can climb?
EXTENSION ACTIVIES
Use distance sensor to stop automatically at finish.
Centre Button Light colour change for “turbo mode” (speed) and “power mode” (strength).
Record times and successes in a results table.
Activity 3: Robot Gym – Fastest & Strongest Challenge
Notes: Pupils might enjoy extending their learning outside lesson time, by taking part in Coding Success: CLUB.